B1: Subroutines
Pascal: procedures
C: Functions
Java: Methods
Section of code: can be invoked repeatedly during program execution
Saves effort, reduces program space
Easier to share code
Can package a specific activity
Provides easy access to thoroughly tested code
In assembly:
Label PROC
…
RET	(return)
Label ENDP
Can be called using call label
PROC/ENDP not part of Intel x86 instruction set
Cannot create procedures using inline assembler
Can call C library functions from inline assembler – code the procedure outside the _asm block

B2: Nested Calls & The Call Stack
CALL records current value of IP (Instruction Pointer) as return address
Puts the subroutine address into IP – corresponding instruction is executed next
RET (at end of subroutine): Retrieves stored return address, puts it back into IP
Storing return address in CPU register/one memory location would only allow for one address
This would be overwritten if a second subroutine was called from the first one
Use a stack – each new call will add a new return address to the top of a stack
They will be retrieved in reverse order – from innermost subroutine, progressing out to main program

B3: Machine Level Stacks
Stack is LIFO, queue is FIFO
Stack push: Push new value onto top of stack
Stack pop: Pop top value from the top of the stack
Stack push/pop: from Intel x86 assembly instructions
Use the ESP stack pointer register – holds address of current top stack item
PUSH: decrements ESP address, so it points to a free space on the stack. Writes item to the memory location that ESP register now points to
POP: Fetches the item addresses by ESP. Increments ESP by correct amount to remove top item
Must ensure redundant items are removed
Stack grows downwards in memory – starts from ending, new items are added to the first numerical memory address. ESP decrements for pushing
EIP (instruction pointer) increases after each normal instruction is executed

Stack can be adjusted – remove items, or reserve extra space. By altering stack pointer (ESP)
E.g. ADD ESP, 8: Add 8 to the current value. Top 8 are discarded
E.g. SUB ESP, 256: Subtract 256 from ESP value. I.e. add space to add 64 more instructions to top of stack

B4: Subroutine Parameters
Simplest type – perform an identical function each time it’s called
2 types of parameters: value, reference
Value: Numeric, ASCII, etc. ‘Pass by value’, e.g. to compare 43 and 29
Reference: “Given two variables, exchange their values”. Pass in the memory addresses of where the variable is stored. ‘Pass by reference’ – the value associated with the variable has to be fetched to use/compare it
Pass variables into a subroutine by using a register: simplest method
Copy the variable’s value into an available CPU register, then call the subroutine
Registers are suitable for passing both value and reference parameters
E.g Pass by Value.
…
Mov eax, first
Mov ebx, second	; CALLING
Call bigger	; SEQUENCE
Mov max, eax
Bigger: proc
Cmp eax, ebx
Jl second_big
Ret
Second_big:
Mov eax, ebx
Ret
Bigger: endp
E.g Pass by Reference
Lea eax, first
Lea ebx, second
Call swap
Swap: proc
Mov temp, [eax]
Mov [eax], [ebx]
Mov [ebx], temp
Ret
Swap: end
Easy to use general-purpose registers when only few parameters need to be passed
Not enough registers for implementing subroutines with arbitrarily large number of parameters
Alternative: Use the memory stack for parameter handling with many objects
E.g. Stack
Push num1
Push num2
Call multiply
Mov result, eaax
Multiply PROC
Pop ebx
Pop eax
Mov tmp, eax
Pop eax
Mul eax, tmp	; multiply 2 values
Push ebx
Ret
Multiply ENDP
B5: Calling External Subroutines for I/O
Can use stack to call external subroutines
Therefore can use C library functions to handle I/O.
E.g. printf(“Hello World\n”;
Expects parameters to be on the stack
Expects string parameter passed by reference
Does not automatically remove parameter from the stack – has to be done manually
Usage within inline assembly language:
#include <stdio.h>
#include <stdlib.h>
Int main (void) {
Char msg[] = “Hello World\n”;	// declare a message using C syntax
_asm {
Lea eax, msg	; put address of string (msg) into eax
Push eax	; Stack the parameter (that holds msg)
Call printf	; Call the external library function. Uses the top value in stack
Pop eax	; Manually pop msg off the stack
}
Return 0;
}
If want to loop, may overwrite registers (e.g. the one used for the count)
Working lines added in red:
Char msg[] = “Hello World\n”;
_asm {
Mov ecx, 10	; set up loop counter
Loop1: push ecx	; save ecx to top of the stack
Lea eax, msg	; put address of string into eax
Push eax	; Stack the parameter
Call printf	; use C library function printf with msg string
Pop eax	; remove msg parameter from the stack
Pop ecx	; restore ecx
Loop loop1	; loop based on ecx
String parameter to printf may contain format specifiers
Format specifiers refer to another parameter, describes how to print it
E.g. int age = 21; char name[] = “Bob”;
Printf(“My name is %s and my age is %d\n”, name, age);
Examples: %d – decimal integer (base 10). %s – string. %c – character. %f – floating point
In-line assembly: need to pass both parameters to do printf(“Number is %d\n”, n);
String, then value of n – therefore need to be pushed onto stack in reverse order
Code:
#include <stdio.h>
#include <stdlib.h>
Int main (void) {
Char msg[] = “Number is %d\n”;
Int n = 157;
_asm {
Push n	; Push the int (157) first
Lea eax, msg	; Store address of msg into eax
Push eax	; Push contents of eax onto the top of the stack
Call printf	; Call library function printf
Add esp, 8	; Add 8 to esp (top of stack pointer – clean 8 bytes from stack)
} return 0;
}
Add is used here to restore the stack, back to what it was before the assembly code.
Top 2 items are no longer in stack, but only one instruction was used
Reduces time complexity
In C syntax, use scanf to read values from the keyboard
E.g. scanf(“%d”, &num);	Formats the input as an integer (decimal)
Need to specify where to store the value – in this example, store it to the variable num
Therefore need to pass the address of the variable if using it inline
Behind-the-scenes:
Char fmt[] = “%d”;
Int num;
_asm {
Lea eax, num
Push eax
Lea eax, fmt
Push eax
Lea eax, fmt
Push eax
Call scanf
Add esp, 8
}
B6: Stack Frames
Stack used to hold return address, and any passed parameters
In example:
Int sub1 (int n)
{
Int x; float y; char z;
}
X, y, z are local variables
Local: Only exist while subroutine active. Used through the stack
Therefore new stack frame created when subroutine is called
Only holds data needed for that specific subroutine
E.g. return address, any parameters, any local variables that are needed
Nested calls – may have many stack frames present simultaneously